## Slide 1
Homework 1 (Due: 27th Oct.)
(1) Which of the following applications are the proper applications of time frequency analysis? Also illustrate the reasons. (a) Signal sampling. (b) Music analysis. (c) Chinese tone analysis. (d) Image analysis. (20 scores)
(2) Suppose that
In what condition the instantaneous frequency of x(t) is invariant with time?
(10 scores)
(3) (a) Why the rectangular windowed STFT may has the side-lobe problem? (b) Why using the triangular window can reduce the side lobe problem?
(10 scores)
(4) Why sometimes it is better to use an asymmetric window instead of a symmetric window for the STFT? (10 scores)
(5) Does Aexp(-Bt2-Ct-D+jEt) satisfy the lower bound of the uncertainty principle? Why? (A, B, C, D, E are real) (15 scores)
Notes: 5

## Slide 2
例子：
dt=0.05;
df=0.05;
t1=[0:dt:10-dt]; t2=[10:dt:20-dt]; t3=[20:dt:30];
t=[0:dt:30];
f=[-5:df:5];
x=[cos(2*pi*t1),cos(6*pi*t2),cos(4*pi*t3)];
B=1;
tic
y=recSTFT(x,t,f,B);
toc
(i) 程式碼要寄給我，(ii) 用 function 的指令寫成函式，
(iii) 自己選一個 input x, 用你們的程式將 output y 算出來並畫出來
(iv) 用 tic 和 toc 的指令來計算程式的 running time
(v) 不可以用 direct implementation 的方法
(6) Write a program for the rectangular short time Fourier transform .
y = recSTFT(x, t, f, B) (35 scores)
x: input, t: samples on t-axis, f: samples on f-axis,
[-B, B]: interval of integration, y: output