## Slide 1
Homework 3 (Due: Dec. 8h)
(1) Write a Matlab program for the Wigner distribution function when the input function has a finite duration.
y = wdf(x, t, f) (35 scores)
x: input, t: samples on t-axis, f: samples on f-axis
(i) 程式碼要寄給我， (ii) 用 function 的指令寫成函式，(iii) 自己選一個 input x， 用你們的程式將 output y 算出來並畫出來， (iv) 用 tic 和 toc 的指令來計算程式的 running time，(v) 程式執行的時間，越短越好 (使用 unbalanced form 有額外加分)
del_t = 0.0125; del_f = 0.05;
t = -9:del_t:9; f = -4:del_f:4;
x = exp(j*t.^2/10-j*3*t).*((t>=-9)&(t<=1))+exp(j*t.^2/2+j*6*t).*exp(-(t-4).^2/10);
tic
y=wdf (x,t,f);
toc
(2) Compared to the Fourier transform, what are the main advantage and the disadvantage of the 3 or 4-parameter atom? (10 scores)

## Slide 2
(3) How do we apply the (a) fractional Fourier transform and the (b) generalized shearing for filter design? (15 scores)
(4) Suppose that the WDFs of x(t) and exp(j(at3+bt2+ct))x(dt +e) are the left and the right figures, respectively. Determine the values of a, b, c, d , e. (15 scores)
(12,5)
(-2,3)
(-2,-3)
(3,3)
(3,-3)
(12,2)
(2,2)
(2,5)
(7,0)
parabola
(5) Among the Gabor transform and the WDF, which one is better for the applications of (a) signal sampling, (b) multiplexing, (c) optical system analysis, and (d) random process analysis? Also illustrate the reasons.
(15 scores)
(6) (a) Why the Fresnel transform of a stationary random process is still a stationary one? (b) Why the linear canonical transform of a white noise is still a white one? (illustration by the WDF instead of mathematical analysis)
(10 scores)